## Slide 1: HeineOS Assignment material: Keyboard
Prof. Dr. Michael Schöttner
Dr. Fabian Ruhland

## Slide 2: PS/2 Keyboard - Components
Keyboard chip inside the keyboard:
  Serial communication with the keyboard controller
  Queries the keyboard via its scan matrix
Keyboard controller on the mainboard:
  Nowadays, integrated inside the South Bridge
  Additional port for a PS/2 mouse
  Uses IRQ1 and IO-Ports 0x60 and 0x64
Modern PC: USB keyboard:
  USB Legacy Support: Backwards compatible
communication via the PS/2 controller
Keyboard chip
Keyboard controller
Clock
Keyboard controller
Ground
Data
+5 Volt
Reset

## Slide 3: PS/2 Keyboard - Scancodes
Keyboards send scancodes (7-bit unique number for each key)
Driver needs to translate scancodes into characters (according to the configured layout)
Lock keys functionality (e.g. Caps Lock) is also implemented inside the driver
Example for an MF II keyboard:

## Slide 4: PS/2 Keyboard - Scancodes
Example: Scancodes and ASCII-codes:
Keyboard controller sends additional information
  Make-Code when pressing/holding a key
  Break-Code when releasing a key
Char | ASCII
( | 40
0 | 48
1 | 49
2 | 50
A | 65
B | 66
a | 97
Key | Scancode
A | 30
a | 30
S | 31
D | 32
Cursor Up | 72
Cursor Down | 80
a | 97

## Slide 5: PS/2 Keyboard - Scancodes
Usually, the following applies:
  Make-Code (key pressed) → Scancode
  Break-Code (key release) → Scancode + 128 (Bit 7 is set)
However, some keys send multiple codes
  For example the function keys (F1-F12)
  Up to three codes per key
Builtin repeat functionality
  Hardware sends Make-Codes multiple times, when a key is held down
Decoding is cumbersome
  HeineOS already contains implemented function fn decode_byte(&mut self, mut code: u8) -> bool
  Returns true if a key has been fully decoded, false if more codes are expected by the controller
  Decoded key is stored in variable Keyboard::gather

## Slide 6: PS/2 Keyboard - Communication
Communication with the keyboard controller works via two I/O-ports:
  Input/Output register (data_port) 0x60
  Status/Control register (control_port) 0x64

## Slide 7: PS/2 Keyboard – Status Register
Access by reading from I/O-port 0x64
  Bit 7: PARE Parity error
  Bit 6: TIM Response timeout
  Bit 5: AUXB Byte available vom auxiliary device (mouse) → Please read byte from output buffer
  Bit 4: KEYL Keyboard available (1) or locked (0)
  Bit 3: C/D Command or data byte written
  Bit 2: SYSF Self test successful
  Bit 1: INPB Input buffer busy → Please wait
  Bit 0: OUTB Byte available → Please read byte from output buffer

## Slide 8: PS/2 Keyboard – Control Register
Access by writing to I/O-port 0x64
  Keyboard controller commands (1 byte)
    0xAA Self test
    0xAE Enable keyboard
    0xED Turn on/off LEDs
    0xF3 Set repeat rate
  Caution: Before sending a command, make sure the input buffer is empty → Check Bit 1 (INPB) in status register
An overview of keyboard commands is given here: https://wiki.osdev.org/PS/2_Keyboard

## Slide 9: PS/2 Keyboard – Reading Keys
Call Keyboard::poll_key_event()
  Calls Keyboard::try_read_next_byte() in a loop until a key is returned
    try_read_next_byte() checks if a byte is available in the output buffer by checking BIT 0 (OUTB) in the status register
    If a byte is available it is decoded using Keyboard::decode_byte()
    If decode_byte() returns true return Keyboard::gather, otherwise return None
Actively reading the keyboard in a loop (polling) is rather inefficient
  Will be replaced by an interrupt based implementation later on in the project

## Slide 10: PS/2 Keyboard – Send Commands
General sequence:
  Wait until the input buffer is empty → Check Bit 1 INPB in status register
  Write the command byte to the data port
  Wait for an answer → Check Bit 0 OUTB in status register
  Read answer from data port
  If the answer is not an ACK (0xFA) abort and return -1
  Otherwise write parameter byte to the data port
  Wait for an answer → Check Bit 0 OUTB in status register
  If the answer is an ACK (0xFA) return 0, othwerwise return -1

## Slide 11: PS/2 Keyboard – Control LEDs
Structure of the parameter byte:
Bit | Meaning
7 | -
6 | -
5 | -
4 | -
3 | -
2 | Caps Lock
1 | Num Lock
0 | Scroll Lock

## Slide 12: PS/2 Keyboard – Repeat Rate
Typematic rate:
  Determines how fast the same scan code is sent, when a key is held down
  Simulates multiple key presses
  Repeat rate is configurable between 2 and 30 repetitions per second
Delay rate:
  Determines the timespan, after which the repetition should start (tolerance ca. 20%)
Code | Delay
00 | ¼ s
01 | ½ s
10 | ¾ s
11 | 1 s

## Slide 13: PS/2 Keyboard – Repeat Rate
Typematic rate:
The codes are calculated using the following formula: Repetitions per second = 1 / (( 8 + A) * 2B * 0.00417) A = Bits 0-2 of code; B = Bits 3-4 of code
Code | Repetitions | Code | Repetitions | Code | Repetitions | Code | Repetitions
11111 | 2.0s | 10111 | 4.0s | 01111 | 8.0s | 00111 | 16.0s
11110 | 2.1s | 10110 | 4.3s | 01110 | 8.6s | 00110 | 17.1s
11101 | 2.3s | 10101 | 4.6s | 01101 | 9.2s | 00101 | 18.5s
11100 | 2.5s | 10100 | 5.0s | 01100 | 10.0s | 00100 | 20.0s
11011 | 2.7s | 10011 | 5.5s | 01011 | 10.9s | 00011 | 21.8s
11010 | 3.0s | 10010 | 6.0s | 01010 | 12.0s | 00010 | 24.0s
11001 | 3.3s | 10001 | 6.7s | 01001 | 13.3s | 00001 | 26.7s
11000 | 3.7s | 10000 | 7.5s | 01000 | 15.0s | 00000 | 30.0s

## Slide 14: PS/2 Keyboard – Repeat Rate
Structure of the full parameter byte:
Bit | Meaning
7 | -
6 | Delay rate
5 | Delay rate
4 | Typematic rate
3 | Typematic rate
2 | Typematic rate
1 | Typematic rate
0 | Typematic rate

## Slide 15: PS/2 Keyboard – Mouse support
Both the mous and the keyboard are connected to the PS/2 controller
Keyboard uses IRQ1 and mous IRQ12
Whether a data byte came from the keyboard or the mouse is signaled via the status register (Bit 5 AUXB)
https://wiki.osdev.org/File:Ps2-kbc.png